## Slide 1: Network awareness in a multiple-network environment
Hidetoshi Yokota
KDDI

## Slide 2: Network-aware Webapps
Choose the right I/F (e.g., 3G, LTE and WiFi)
  By content type
  By URL
Choose the right content based on the network interface
  High quality content is selected when WiFi is used
Adjust traffic volume according to the interface usage
  Skip downloading when the NW I/F is heavily used
Adjust traffic volume according to the network condition
  Skip downloading when packet loss rate is high
<h1> … </h1>
<video> </video>
<audio> </audio>
<a href=xyz.htm>
<a href=abc.htm>
WiFi
Best effort bearer
(QCI=8, non-GBR)
QoS bearer
(QCI=1, GBR)
3G
NW I/F
<body>
</body>
<body>
</body>

## Slide 3: Possible approaches
Web API to retrieve more detailed information on the network interface(s) for more efficient network usage
  Network information obtained solely by the terminal (e.g., Cellular and WiFi base stations, signal strength, error rate, throughput)
  Network information obtained by cooperating with the network (e.g. access network load, backhaul load, congested APs) via 3GPP ANDSF or WFA Hotspot 2.0
   Extension to Network information API?
Web API to control network interfaces for fine-grained network selection
  Network interface control should support not only open/close, but also attachment to a specific base station in WiFi network, establishment of a dedicated bearer in cellular network, etc.
  Support of concurrent usage of multiple networks and access network selection based on the content type (video/voice/text)
  Extension to/new features for Network interface API?